## Slide 1
SIMATS ENGINEERING
ASSESSMENT TOOL 1
COURSE CODE: CSA07
COURSE NAME: COMPUTER
NETWORKS
COURSE OUTCOME COVERED
CO2: Configure IP addressing schemes, subnetting, and basic routing techniques using simulation tool, for efficient network design and topology. (BL3)
Assessment Tool Weightage: 40%
Annexure A
ANALYTICAL PROBLEM SOLVING
Code of Conduct:
I GODDAVULA NITISH KANTH (192512232) (Name / Reg No) certify that this submission is my original work and that I have adhered to the guidelines specified for this assessment.
I understand that any violation of academic integrity rules will result in disciplinary action.
Signature of the student: G.NITISH KANTH

## Slide 2
Annexure A
ANALYTICAL PROBLEM SOLVING
1. Suppose we want to transmit the message 11100011 and protect it from errors using the CRC polynomial X3+1.
i.) Use polynomial long division to determine the message that should be transmitted.
ii) Suppose the leftmost bit of the message is inverted due to noise on the transmission link. What is the result of the receiver's CRC calculation? How does the receiver know that an error has occurred?
SOLUTION:
Given:
Message: 11100011
Generator Polynomial: x
3
+ 1
x3+1
Binary Generator: 1001
CRC Calculation
Append 3 zeros (degree of polynomial = 3):
11100011 → 11100011000
Perform modulo-2 division by 1001. CRC Remainder = 100
Hence, the transmitted message is: 11100011100
11100011100
Error Detection
If the leftmost bit is inverted during transmission:
Transmitted: 11100011100
Received: 01100011100
Dividing the received message by 1001 gives:

## Slide 3
Remainder = 001
Since the remainder is not 000, the receiver detects that an error has occurred.
Final Answer
CRC: 100
Transmitted message: 11100011100 Received remainder after error: 001
Conclusion: Non-zero remainder indicates a transmission error.
2. a) A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
b) A network has a bandwidth of 3000 Hz (300 to 3300 Hz) assigned communications. The signal- to-noise ratio is 3162. Find the channel capacity SOLUTION:
for data
(a) Throughput of the Network
Given:
Bandwidth = 10 Mbps
Frames transmitted = 12,000 frames/minute Frame size = 10,000 bits
Formula:
Throughput = (Frames × Bits per frame) / Time
Calculation:
Throughput = (12,000 × 10,000) / 60
= 120,000,000 / 60
= 2,000,000 bps
= 2 Mbps
Answer: The throughput of the network is 2 Mbps.
(b) Channel Capacity
Given:
Bandwidth (B) = 3000 Hz
Signal-to-Noise Ratio (S/N) = 3162

## Slide 4
Formula (Shannon Capacity):
C = B × log₂(1 + S/N)
Calculation:
C = 3000 × log₂(3163)
≈ 3000 × 11.63
≈ 34,890 bps
≈ 34.9 kbps
Answer: The channel capacity is 34.9 kbps.
3. A multispecialty hospital uses wireless patient-monitoring devices to continuously transmit patients' heart rate and blood pressure readings to a central monitoring station. Since the data is transmitted over a wireless channel, electromagnetic interference occasionally changes one bit during transmission. To ensure that doctors receive accurate patient information without waiting for retransmission, the hospital implements the Hamming (12,8) error-correcting code.
SOLUTION:
Hamming (12,8) Code – Hospital Scenario
Problem:
A multispecialty hospital uses wireless patient-monitoring devices to continuously send patients' heart rate and blood pressure readings to a central monitoring station. Due to electromagnetic interference, a single-bit error may occur during data transmission. To ensure accurate data without retransmission, the hospital uses the Hamming (12,8) error-correcting code.
Solution:
The Hamming (12,8) code converts every 8-bit data into a 12-bit codeword by adding 4 parity bits.
During transmission, if a single bit is changed, the parity bits help the receiver detect the exact position of the error.
The receiver automatically corrects the erroneous bit without asking the sender to retransmit the data.
This enables continuous and reliable monitoring of patients, even in the presence of wireless interference.
Advantages:
Detects and corrects single-bit errors. Eliminates the need for retransmission. Reduces communication delay.
Improves the reliability and accuracy of patient-monitoring data.

## Slide 5
Ensures doctors receive correct patient information for timely medical decisions.
Conclusion:
By using the Hamming (12,8) error-correcting code, the hospital ensures that patient data is transmitted accurately and efficiently. Even if a single-bit error occurs due to electromagnetic interference, the receiver can detect and correct it automatically, providing reliable real-time healthcare monitoring.
4. a) A company uses the IP address 172.16.10.0/24 and has implemented subnetting using a
/27 subnet mask for its internal departments. Using the given subnet mask, apply subnetting techniques to calculate the total number of subnets created and the number of usable hosts per subnet. Determine the subnet to which the IP address 172.16.10.78 belongs. Identify the network address and broadcast address for that subnet. Also, determine whether the IP address 172.16.10.95 falls within the same subnet range based on the given configuration.
b ) A n e t w o r k u s e s t h e I n t e r n e t P r o t o c o l v e r s i o n 6 a d d r e s s 2001:0db8:0000:0000:0000:ff00:0042:8329. Apply IPv6 addressing rules to compress the given address into its shortest form and then expand the compressed address back to its full
notation. Using a prefix length of /64, determine the network prefix of the given address. Also, calculate the total number of possible host addresses available within this network based on the given prefix length.
SOLUTION:
(a) IPv4 Subnetting
Given:
Network: 172.16.10.0/24
Subnet Mask: /27
Step 1: Number of Subnets
Borrowed bits = 27 − 24 = 3 Number of subnets = 2³ = 8 Step 2: Hosts per Subnet Host bits = 32 − 27 = 5
Total hosts = 2⁵ = 32 Usable hosts = 32 − 2 = 30
Step 3: Find the Subnet of 172.16.10.78

## Slide 6
Subnet ranges:
172.16.10.0 – 31
172.16.10.32 – 63
172.16.10.64 – 95
172.16.10.96 – 127
172.16.10.128 – 159
172.16.10.160 – 191
172.16.10.192 – 223
172.16.10.224 – 255
IP 172.16.10.78 belongs to the subnet 172.16.10.64/27.
Network Address = 172.16.10.64
Broadcast Address = 172.16.10.95
Usable Host Range = 172.16.10.65 – 172.16.10.94
Step 4: Check IP 172.16.10.95
172.16.10.95 is the broadcast address of the subnet. Therefore, it does not represent a usable host.
Answer:
Total Subnets = 8
Usable Hosts/Subnet = 30 Subnet = 172.16.10.64/27
Network Address = 172.16.10.64 Broadcast Address = 172.16.10.95
IP 172.16.10.95 is the broadcast address, so it is not a usable host.
(b) IPv6 Addressing
Given Address:
2001:0db8:0000:0000:0000:ff00:0042:8329
Compressed Form
2001:db8::ff00:42:8329
Expanded Form
2001:0db8:0000:0000:0000:ff00:0042:8329
Network Prefix (/64)
Network Prefix:
2001:0db8:0000:0000::/64
Number of Host Addresses

## Slide 7
Host bits = 128 − 64 = 64
Total Hosts = 2⁶⁴
= 18,446,744,073,709,551,616
Answer:
Compressed Address = 2001:db8::ff00:42:8329
Expanded Address = 2001:0db8:0000:0000:0000:ff00:0042:8329 Network Prefix = 2001:db8:0:0::/64
Total Host Addresses = 2⁶⁴ (18,446,744,073,709,551,616)
5. A university is conducting an online semester examination for 8,000 students simultaneously. At exactly 10:00 AM, the examination server begins transmitting encrypted question papers to all students. The university server is connected through a
10 Gbps high-speed network, while students access the examination portal using different internet connections such as fiber broadband (100 Mbps), home Wi-Fi (20 Mbps), and mobile networks (5–10 Mbps). During the first few minutes of the examination, many students with slower internet connections report incomplete downloads, repeated retransmissions, delayed acknowledgments, and temporary freezing of the examination portal. Network administrators observe that the server continues transmitting data at a high rate even though several student devices are unable to receive and process packets at the same speed. This results in receiver buffer overflow, unnecessary retransmissions, increased network traffic, and delays in delivering the question papers. Analyze the above scenario and identify the primary networking problem. Explain how the mismatch between the sender's transmission speed and the receiver's processing capability affects communication.
SOLUTION:
Primary Networking Problem:
The primary networking problem is Flow Control. Flow control is used to regulate the rate at which the sender transmits data so that the receiver can process it without being overwhelmed.
Explanation:
The university server is connected through a 10 Gbps network and sends encrypted question papers to 8,000 students simultaneously.
Students use different internet connections, such as 100 Mbps fiber, 20 Mbps Wi-Fi, and 5–10 Mbps mobile networks.
Since many students have slower connections, they cannot receive and process data as quickly as the server transmits it.

## Slide 8
This mismatch between the sender's transmission speed and the receiver's processing capability causes the receiver's buffer to overflow.
As a result, packets are lost, acknowledgments are delayed, and the sender retransmits the lost packets.
These unnecessary retransmissions increase network traffic, leading to congestion, incomplete downloads, temporary freezing of the examination portal, and delays in delivering the question papers.
Solution:
Flow control mechanisms, such as the Sliding Window Protocol, allow the receiver to inform the sender about the amount of data it can accept.
The sender adjusts its transmission rate based on the receiver's available buffer space.
This prevents buffer overflow, reduces packet loss and retransmissions, improves network efficiency, and ensures that all students receive the examination papers reliably and on time.
Conclusion:
The issue arises because the sender transmits data much faster than some receivers can handle. By implementing effective flow control, the network can balance the transmission rate with the receiver's processing speed, ensuring smooth, reliable, and efficient communication during the online examination.

## Slide 9
RUBRICS FOR CALCULATION
Criteria | Weightage | Level 4 (Exemplary) | Level 3 (Proficient) | Level 2 (Developing) | Level 1 (Beginning)
Problem Understandi n g | 20% | Clearly interprets problem, identifies all parameters and requirement s accurately | Understan d s problem with minor gaps | Partial understandi ng ; misses key elements | Misinterpre ts or unable to understand problem
Method Selection | 20% | Selects most appropriate method/ formul a with strong justification | Selects correct method with minor errors | Inappropriat e or partially correct method | Unable to select method
Soluti on Proce ss | 25% | Logical, systematic steps with correct approach throughout | Mostly correct steps with minor mistakes | Disorganized steps; multiple errors | No clear proce ss
Accuracy of Calculatio n | 20% | All calculations accurate; correct final answer | Minor calculati on errors | Frequent errors; incorrect final answer | No valid calculations
Interpretation of Results | 15% | Clearly interprets results with units and engineering relevance | Basic interpretati o n with minor omissions | Limited or unclear interpretati on | No interpretati o n